## Slide 1
Pile type | Concrete filled steel pipe piles | Composite piles | Precast concrete (including prestressed) | Cast in place (thin shell driven with mandrels) | Auger placed pressure-injected concrete (grout) piles
Disadvantages | High initial cost Displacement for closed- end pipe | Difficult to attain good joint between two materials | Difficult to handle unless prestressed High initial cost Considerable displacement Prestressed difficult to splice | Difficult to splice after concreting Redriving not recommended Thin shell vulnerable during driving Considerable displacement | Dependence on workmanship Not suitable in compressible soil
Advantages | Best control during installation No displacement for open-end installation Open-end pipe best against obstructions High load capacitites Easy to splice | Considerable length can be provided at comparatively low cost | High load capacities Corrosion resistance can be attained Hard driving possible | Initial economy Taped sections provide higher bearing resistance in granular stratum | Freedom from noise and vibration Economy High skin friction No splicing
Remarks | Provides high bending resistance where unsupported length is loaded laterally | The weakest of any material used shall govern allowable stresses and capacity | Cylinder piles in particular are suited for bending resistance | Best suited for medium- load friction piles in granular materials | Patented method
TABLE 6.15 Typical Pile Characteristics and Uses (Continued)
Typical illustrations |  |  |  |  |