## Slide 1
1. Spread Footings, Combined Footings, and Strip Footings. These types of shallow foundations are probably the most common types of building foundations. Examples of these types of footings are shown in Fig. 6.40.
2. Mat Foundation. Examples of mat foundations are shown in Fig. 6.41. Based on economic considerations, mat foundations are constructed for the following reasons:
(a) Large Individual Footings. A mat foundation is often constructed when the sum of individual footing areas exceeds about one-half of the total foundation area.
(b) Cavities or Compressible Lenses. A mat foundation can be used when the subsurface exploration indicates that there will be unequal settlement caused by small cavities or compressible lenses below the foundation. A mat foun- dation would tend to span over the small cavities or weak lenses and create a more uniform settlement condition.
(c) Shallow Settlements. A mat foundation can be recommended when shallow settlements predominate and the mat foundation would minimize differential settlements.
(d ) Unequal Distribution of Loads. For some structures, there can be a large difference in building loads acting on different areas of the foundation. Con- ventional spread footings could be subjected to excessive differential settle-
ment, but a mat foundation would tend to distribute the unequal building
loads and reduce the differential settlements.
(e) Hydrostatic Uplift. When the foundation will be subjected to hydrostatic
uplift due to a high groundwater table, a mat foundation could be used to
resist the uplift forces.
FIGURE 6.40 Examples of shallow foundations:
(a)combined footing;
(b) com- bined trapezoidal footing;
(c) cantilever or strap footing;
(d ) octagonal footing;
(e) eccentric loaded footing with resultant coincident with area so soil pressure is uni- form.