## Slide 1
6.6 BEARING CAPACITY ANALYSES
A bearing capacity failure is defined as a foundation failure that occurs when the
shear stresses in the soil exceed the shear strength of the soil. Bearing capacity
failures of foundations can be grouped into three categories (A. B. Vesic´, ‘‘Bearing
Capacity of Deep Foundations in Sand,’’ Highway Research Record, no. 39):
1. General Shear (Fig. 6.24). As shown in Fig. 6.24, a general shear failure involves
total rupture of the underlying soil. There is a continuous shear failure
of the soil (solid lines) from below the footing to the ground surface. When the
load is plotted versus settlement of the footing, there is a distinct load at which
the foundation fails (solid circle), and this is designated Qult. The value of Qult
divided by the width (B) and length (L) of the footing is considered to be the
‘‘ultimate bearing capacity’’ (qult) of the footing. The ultimate bearing capacity
has been defined as the bearing stress that causes a sudden catastrophic failure
of the foundation. Note in Fig. 6.24 that a general shear failure ruptures and
pushes up the soil on both sides of the footing. For actual failures it the field,
the soil is often pushed up on only one side of the footing with subsequent
tilting of the structure. A general shear failure occurs for soils that are in a dense
or hard state.
2. Punching Shear (Fig. 6.25). As shown in Fig. 6.25, a punching shear failure
does not develop the distinct shear surfaces associated with a general shear
failure. For punching shear, the soil outside the loaded area remains relatively
uninvolved and there is minimal movement of soil on both sides of the footing.

## Slide 2
FIGURE 6.24 General shear foundation failure for soil in a dense or hard state. (Adapted from A. B. Vesic´, ‘‘Bearing Capacity of Deep Foundations in Sand,’’ High- way Research Record, no. 39.)