## Slide 1
5.5.2 Reactions
As an example of the application of the equations of equilibrium (Art. 5.2.1) to the
determination of the reactions of a statically determinate beam, we shall compute
FIGURE 5.17 Beam with overhangs loaded with both uniform and concentrated loads.
the reactions of the 60-ft-long beam with overhangs in Fig. 5.17. This beam carries a uniform load of 200 lb / lin ft over its entire length and several concentrated
loads. The supports are 36 ft apart.
To find reaction R1, we take moments about R2 and equate the sum of the moments
to zero (clockwise rotation is considered positive, counterclockwise, negative):
-2000 X 48 + 36R1 - 4000 X 30 - 6000 X 18 + 3000 X 12-200 X 60 X 18 = 0
R1 = 14,000 lb