## Slide 1
6.7 RETAINING WALLS
A retaining wall is defined as a structure whose primary purpose is to provide lateral support for soil or rock. In some cases, such as basement walls and certain types of bridge abutments, it may also support vertical loads. The more common types of retaining walls are shown in Fig. 6.33 and include gravity walls, cantilevered walls, counterfort walls, and crib walls.
Gravity retaining walls are routinely built of plain concrete or stone, and the wall depends primarily on its massive weight to resist failure from overturning and sliding. Counterfort walls consist of a footing, a wall stem, and intermittent vertical ribs (called counterforts) that tie the footing and wall stem together. Crib walls consist of interlocking concrete members that form cells which are then filled with compacted soil.
FIGURE 6.33 Common types of retaining walls: (a) Gravity walls of stone, brick, or plain concrete. Weight provides overturning and sliding stability; (b) can- tilevered wall; (c) counterfort, or buttressed, wall. If backfill covers counterforts, the wall is termed a counterfort retaining wall; (d ) crib wall; (e) semigravity wall (often steel reinforcement is used); ( f ) bridge abutment. (Reproduced from J. E. Bowles, ‘‘Foundation Analysis and Design,’’ 3d ed., McGraw-Hill Publishing Co., New York, with permission of McGraw-Hill, Inc.)