## Slide 1: Understanding the TCP/IP Protocol Suite
Industry standard
Enables enterprise networking and connectivity

## Slide 2: Advantages of TCP/IP in a Microsoft Windows 2000 Configuration
Provides a routable networking protocol
Connects dissimilar systems
Supports a robust, scaleable, cross-platform client/server framework
Supports Windows Sockets (Winsock)
Provides access to Internet resources
<number>

## Slide 3: Four Layers

## Slide 4: Configuring TCP/IP to Use a Static Address
By default, client computers running Microsoft Windows 2000, Microsoft Windows 98, or Microsoft Windows 95 obtain TCP/IP configuration information automatically.
Some computers should always be assigned a static IP address, for example the computer running the DHCP Service.

## Slide 5: Options Used in Configuring a Static TCP/IP Address

## Slide 6: Configuring TCP/IP to Obtain an IP Address Automatically
07/29/26 05:09
<footer>
<number>

## Slide 7: Using Automatic Private IP Addressing
Extension of dynamic IP address assignment for LAN adapters
Enables configuration of IP addresses without
  Using static IP address assignment
  Installing the DHCP Service
Configure network LAN adapter to Obtain An IP Address Automatically

## Slide 8: Steps in Automatic Private IP Addressing

## Slide 9: Disabling Automatic Private IP Addressing
Enabled by default.
Add the IPAutoconfigurationEnabled value to the HKEY_LOCAL_MACHINE\SYSTEM\CurrentControlSet\ Services\Tcpip\Parameters\Interfaces\Adapter subkey.
Set IPAutoconfigurationEnabled value to 0.

## Slide 10: Using TCP/IP Utilities

## Slide 11: Using Ipconfig
Use ipconfig /all to verify the TCP/IP configuration parameters on a host.
Use ipconfig /all | more to prevent the ipconfig output from scrolling off the screen.

## Slide 12: Example 1, Understanding Ipconfig /all
If the configuration is initialized
  Ipconfig displays the IP address and subnet mask.
  Ipconfig displays the default gateway if it is assigned.

## Slide 13: Example 2, Understanding Ipconfig /all
If a duplicate IP address exists
  Ipconfig indicates IP address is configured.
  Subnet mask is 0.0.0.0.

## Slide 14: Example 3, Understanding Ipconfig /all
No server running the DHCP Service on the network
  IP address provided by Automatic Private IP Addressing
  IP address is 169.254.0.0 through 169.254.255.255

## Slide 15: Using Ping
Use to test connectivity
Use to determine if a host is available and functional

## Slide 16: Using Ipconfig and Ping

## Slide 17: Introduction to NWLink
NWLink IPX/SPX/NetBIOS-compatible transport protocol
Microsoft’s implementation of Novell’s NetWare IPX/SPX protocol
Commonly used where
  Clients running Microsoft operating systems access resources on NetWare servers
  Clients running NetWare access resources on computers running Microsoft operating systems

## Slide 18: Understanding NWLink Features
Supports communications with NetWare networks
Supports sockets and NetBIOS over IPX
Provides NetWare clients with access to Windows 2000 Servers

## Slide 19: Installing NWLink

## Slide 20: Configuring NWLink
Frame type
Network number
Internal network number

## Slide 21: Configuring NWLink (continued)
By default, Windows 2000 detects a frame type and a network number.
Windows 2000 provides a generic network number.
Each network adapter card bound to NWLink in a computer requires a frame type and a network number.

## Slide 22: Frame Type
The frame type defines the way that the network adapter card formats data.
The NWLink frame type should match the frame type on the NetWare server.
You can manually configure the frame type.

## Slide 23: Topologies and Frame Types
Ethernet supports Ethernet II, 802.3, 802.2, and SNAP.
Token Ring topology supports 802.5 and SNAP.
FDDI supports 802.2 and SNAP.

## Slide 24: Network Numbers
Each frame type configured on a network adapter card requires a network number.
The network number must be unique for each network segment.
Computers on a segment using the same frame type must use the same network number to communicate with each other.
Use Registry Editor to manually specify a network number.

## Slide 25: Internal Network Numbers
Uniquely identifies a computer on the network for internal routing
Eight-digit hexadecimal number that is set to 00000000 by default

## Slide 26: Manually Assign an Internal Network Number if
FPNW is installed and there are multiple frame types on a single adapter
FPNW is installed and NWLink is bound to multiple adapters in the computer
An application is using the NetWare Service Advertising Protocol (SAP)

## Slide 27: Introduction to NetBEUI
Developed for LANs with 20 to 200 computers
Small, fast, and efficient protocol
Not routable

## Slide 28: NetBEUI Capabilities
Connection-oriented and connectionless communication between computers
Self-configuration and self-tuning
Error protection
Small memory overhead

## Slide 29: NetBEUI Limitations
Designed for departmental-sized LANs
Must connect computers running Windows 2000 and NetBEUI by using bridges
Relies on broadcasts for many of its functions

## Slide 30: DLC

## Slide 31: AppleTalk Protocol
Allows computers running Windows 2000 Server and Apple Macintosh clients to share files and printers.
A computer running Windows 2000 Services for Macintosh must be available on the network.

## Slide 32: Network Monitor Driver 2
Collects and displays statistics about activity detected by the network card.
View these statistics on a computer running Network Monitor Agent Service.
Use Microsoft Systems Management Server and Network Monitor to collect statistics from computers running Network Monitor Agent.

## Slide 33: Introduction to Network Bindings

## Slide 34: Combining Network Bindings
You can select which protocols are bound to the network adapter cards.
When adding network software, Windows 2000 automatically binds all dependent network components accordingly.
Network Driver Interface Specification (NDIS) 5 provides the local security database that Windows 2000 uses to validate the logon information.

## Slide 35: Configuring Network Bindings
In the Network And Dial-Up Connections window, click Advanced, and then click Advanced Settings to configure network bindings.
Only an experienced network administrator who is familiar with the requirements of the network software should attempt to change binding settings.

## Slide 36: Specifying Binding Order
You can specify binding order to optimize network performance.
To specify the binding order, in the Network And Dial-Up Connections window, click Advanced, and then click Advanced Settings.