## Slide 1
Chapter 7 Multimedia Networking
A note on the use of these ppt slides:
We’re making these slides freely available to all (faculty, students, readers). They’re in PowerPoint form so you can add, modify, and delete slides (including this one) and slide content to suit your needs. They obviously represent a lot of work on our part. In return for use, we only ask the following:
If you use these slides (e.g., in a class) in substantially unaltered form, that you mention their source (after all, we’d like people to use our book!)
If you post any slides in substantially unaltered form on a www site, that you note that they are adapted from (or perhaps identical to) our slides, and note our copyright of this material.
Thanks and enjoy! JFK / KWR
All material copyright 1996-2006
J.F Kurose and K.W. Ross, All Rights Reserved
Computer Networking: A Top Down Approach Featuring the Internet, 3rd edition. Jim Kurose, Keith Ross Addison-Wesley, July 2004.

## Slide 2: Multimedia, Quality of Service: What is it?
Multimedia applications: network audio and video
(“continuous media”)
network provides application with level of performance needed for application to function.
QoS

## Slide 3: Chapter 7: Goals
Principles
Classify multimedia applications
Identify the network services the apps need
Making the best of best effort service
Mechanisms for providing QoS
Protocols and Architectures
Specific protocols for best-effort
Architectures for QoS

## Slide 4: Chapter 7 outline
7.1 Multimedia Networking Applications
7.2 Streaming stored audio and video
7.3 Real-time Multimedia: Internet Phone study
7.4 Protocols for Real-Time Interactive Applications
  RTP,RTCP,SIP
7.5 Distributing Multimedia: content distribution networks
7.6 Beyond Best Effort
7.7 Scheduling and Policing Mechanisms
7.8 Integrated Services and Differentiated Services
7.9 RSVP

## Slide 5: MM Networking Applications
Fundamental characteristics:
Typically delay sensitive
  end-to-end delay
  delay jitter
But loss tolerant: infrequent losses cause minor glitches
Antithesis of data, which are loss intolerant but delay tolerant.
Classes of MM applications:
1) Streaming stored audio and video
2) Streaming live audio and video
3) Real-time interactive audio and video
  Jitter is the variability
  of packet delays within
  the same packet stream

## Slide 6: Streaming Stored Multimedia
Streaming:
media stored at source
transmitted to client
streaming: client playout begins before all data has arrived
timing constraint for still-to-be transmitted data: in time for playout

## Slide 7: Streaming Stored Multimedia: What is it?
1. video
recorded
2. video
sent
3. video received,
played out at client
Cumulative data
streaming: at this time, client
playing out early part of video,
while server still sending later
part of video
network
delay
time

## Slide 8: Streaming Stored Multimedia: Interactivity
VCR-like functionality: client can pause, rewind, FF, push slider bar
  10 sec initial delay OK
  1-2 sec until command effect OK
  RTSP often used (more later)
timing constraint for still-to-be transmitted data: in time for playout

## Slide 9: Streaming Live Multimedia
Examples:
Internet radio talk show
Live sporting event
Streaming
playback buffer
playback can lag tens of seconds after transmission
still have timing constraint
Interactivity
fast forward impossible
rewind, pause possible!

## Slide 10: Interactive, Real-Time Multimedia
end-end delay requirements:
  audio: < 150 msec good, < 400 msec OK
    includes application-level (packetization) and network delays
    higher delays noticeable, impair interactivity
session initialization
  how does callee advertise its IP address, port number, encoding algorithms?
applications: IP telephony, video conference, distributed interactive worlds

## Slide 11: Multimedia Over Today’s Internet
TCP/UDP/IP: “best-effort service”
no guarantees on delay, loss
Today’s Internet multimedia applications
use application-level techniques to mitigate
(as best possible) effects of delay, loss
But you said multimedia apps requires
QoS and level of performance to be
effective!
?
?
?
?
?
?
?
?
?
?
?

## Slide 12: How should the Internet evolve to better support multimedia?
Integrated services philosophy:
Fundamental changes in Internet so that apps can reserve end-to-end bandwidth
Requires new, complex software in hosts & routers
Laissez-faire
no major changes
more bandwidth when needed
content distribution, application-layer multicast
  application layer
Differentiated services philosophy:
Fewer changes to Internet infrastructure, yet provide 1st and 2nd class service.
What’s your opinion?

## Slide 13: A few words about audio compression
Analog signal sampled at constant rate
  telephone: 8,000 samples/sec
  CD music: 44,100 samples/sec
Each sample quantized, i.e., rounded
  e.g., 28=256 possible quantized values
Each quantized value represented by bits
  8 bits for 256 values
Example: 8,000 samples/sec, 256 quantized values --> 64,000 bps
Receiver converts it back to analog signal:
  some quality reduction
Example rates
CD: 1.411 Mbps
MP3: 96, 128, 160 kbps
Internet telephony: 5.3 - 13 kbps

## Slide 14: A few words about video compression
Video is sequence of images displayed at constant rate
  e.g. 24 images/sec
Digital image is array of pixels
Each pixel represented by bits
Redundancy
  spatial
  temporal
Examples:
MPEG 1 (CD-ROM) 1.5 Mbps
MPEG2 (DVD) 3-6 Mbps
MPEG4 (often used in Internet, < 1 Mbps)
Research:
Layered (scalable) video
  adapt layers to available bandwidth

## Slide 15: Chapter 7 outline
7.1 Multimedia Networking Applications
7.2 Streaming stored audio and video
7.3 Real-time Multimedia: Internet Phone study
7.4 Protocols for Real-Time Interactive Applications
  RTP,RTCP,SIP
7.5 Distributing Multimedia: content distribution networks
7.6 Beyond Best Effort
7.7 Scheduling and Policing Mechanisms
7.8 Integrated Services and Differentiated Services
7.9 RSVP

## Slide 16: Streaming Stored Multimedia
Application-level streaming techniques for making the best out of best effort service:
  client side buffering
  use of UDP versus TCP
  multiple encodings of multimedia
jitter removal
decompression
error concealment
graphical user interface w/ controls for interactivity
Media Player

## Slide 17: Internet multimedia: simplest approach
audio, video not streamed:
no, “pipelining,” long delays until playout!
audio or video stored in file
files transferred as HTTP object
  received in entirety at client
  then passed to player

## Slide 18: Internet multimedia: streaming approach
browser GETs metafile
browser launches player, passing metafile
player contacts server
server streams audio/video to player

## Slide 19: Streaming from a streaming server
This architecture allows for non-HTTP protocol between server and media player
Can also use UDP instead of TCP.

## Slide 20: Streaming Multimedia: Client Buffering
constant bit
rate video
transmission
Cumulative data
time
variable
network
delay
client video
reception
constant bit
rate video
playout at client
client playout
delay
buffered
video
Client-side buffering, playout delay compensate for network-added delay, delay jitter

## Slide 21: Streaming Multimedia: Client Buffering
Client-side buffering, playout delay compensate for network-added delay, delay jitter
buffered
video
variable fill
rate, x(t)
constant
drain
rate, d

## Slide 22: Streaming Multimedia: UDP or TCP?
UDP
server sends at rate appropriate for client (oblivious to network congestion !)
  often send rate = encoding rate = constant rate
  then, fill rate = constant rate - packet loss
short playout delay (2-5 seconds) to compensate for network delay jitter
error recover: time permitting
TCP
send at maximum possible rate under TCP
fill rate fluctuates due to TCP congestion control
larger playout delay: smooth TCP delivery rate
HTTP/TCP passes more easily through firewalls

## Slide 23: Streaming Multimedia: client rate(s)
Q: how to handle different client receive rate capabilities?
  28.8 Kbps dialup
  100Mbps Ethernet
A: server stores, transmits multiple copies of video, encoded at different rates
1.5 Mbps encoding
28.8 Kbps encoding

## Slide 24: User Control of Streaming Media: RTSP
HTTP
Does not target multimedia content
No commands for fast forward, etc.
RTSP: RFC 2326
Client-server application layer protocol.
For user to control display: rewind, fast forward, pause, resume, repositioning, etc…
What it doesn’t do:
does not define how audio/video is encapsulated for streaming over network
does not restrict how streamed media is transported; it can be transported over UDP or TCP
does not specify how the media player buffers audio/video

## Slide 25: RTSP: out of band control
FTP uses an “out-of-band” control channel:
A file is transferred over one TCP connection.
Control information (directory changes, file deletion, file renaming, etc.) is sent over a separate TCP connection.
The “out-of-band” and “in-band” channels use different port numbers.
RTSP messages are also sent out-of-band:
RTSP control messages use different port numbers than the media stream: out-of-band.
  Port 554
The media stream is considered “in-band”.

## Slide 26: RTSP Example
Scenario:
metafile communicated to web browser
browser launches player
player sets up an RTSP control connection, data connection to streaming server

## Slide 27: Metafile Example
<title>Twister</title>
<session>
<group language=en lipsync>
<switch>
<track type=audio
e="PCMU/8000/1"
src = "rtsp://audio.example.com/twister/audio.en/lofi">
<track type=audio
e="DVI4/16000/2" pt="90 DVI4/8000/1"
src="rtsp://audio.example.com/twister/audio.en/hifi">
</switch>
<track type="video/jpeg"
src="rtsp://video.example.com/twister/video">
</group>
</session>

## Slide 28: RTSP Operation

## Slide 29: RTSP Exchange Example
C: SETUP rtsp://audio.example.com/twister/audio RTSP/1.0
Transport: rtp/udp; compression; port=3056; mode=PLAY
S: RTSP/1.0 200 1 OK
Session 4231
C: PLAY rtsp://audio.example.com/twister/audio.en/lofi RTSP/1.0
Session: 4231
Range: npt=0-
C: PAUSE rtsp://audio.example.com/twister/audio.en/lofi RTSP/1.0
Session: 4231
Range: npt=37
C: TEARDOWN rtsp://audio.example.com/twister/audio.en/lofi RTSP/1.0
Session: 4231
S: 200 3 OK

## Slide 30: Chapter 7 outline
7.1 Multimedia Networking Applications
7.2 Streaming stored audio and video
7.3 Real-time Multimedia: Internet Phone case study
7.4 Protocols for Real-Time Interactive Applications
  RTP,RTCP,SIP
7.5 Distributing Multimedia: content distribution networks
7.6 Beyond Best Effort
7.7 Scheduling and Policing Mechanisms
7.8 Integrated Services and Differentiated Services
7.9 RSVP

## Slide 31: Real-time interactive applications
PC-2-PC phone
  instant messaging services are providing this
PC-2-phone
  Dialpad
  Net2phone
videoconference with Webcams
Going to now look at a PC-2-PC Internet phone example in detail

## Slide 32: Interactive Multimedia: Internet Phone
Introduce Internet Phone by way of an example
speaker’s audio: alternating talk spurts, silent periods.
  64 kbps during talk spurt
pkts generated only during talk spurts
  20 msec chunks at 8 Kbytes/sec: 160 bytes data
application-layer header added to each chunk.
Chunk+header encapsulated into UDP segment.
application sends UDP segment into socket every 20 msec during talkspurt.

## Slide 33: Internet Phone: Packet Loss and Delay
network loss: IP datagram lost due to network congestion (router buffer overflow)
delay loss: IP datagram arrives too late for playout at receiver
  delays: processing, queueing in network; end-system (sender, receiver) delays
  typical maximum tolerable delay: 400 ms
loss tolerance: depending on voice encoding, losses concealed, packet loss rates between 1% and 10% can be tolerated.

## Slide 34: Delay Jitter
constant bit
rate
transmission
Cumulative data
time
variable
network
delay
(jitter)
client
reception
constant bit
rate playout
at client
client playout
delay
buffered
data
Consider the end-to-end delays of two consecutive packets: difference can be more or less than 20 msec

## Slide 35: Internet Phone: Fixed Playout Delay
Receiver attempts to playout each chunk exactly q msecs after chunk was generated.
  chunk has time stamp t: play out chunk at t+q .
  chunk arrives after t+q: data arrives too late for playout, data “lost”
Tradeoff for q:
  large q: less packet loss
  small q: better interactive experience

## Slide 36: Fixed Playout Delay
Sender generates packets every 20 msec during talk spurt.
First packet received at time r
First playout schedule: begins at p
Second playout schedule: begins at p’

## Slide 37: Adaptive Playout Delay, I
Dynamic estimate of average delay at receiver:
where u is a fixed constant (e.g., u = .01).
Goal: minimize playout delay, keeping late loss rate low
Approach: adaptive playout delay adjustment:
  Estimate network delay, adjust playout delay at beginning of each talk spurt.
  Silent periods compressed and elongated.
  Chunks still played out every 20 msec during talk spurt.

## Slide 38: Adaptive playout delay II
Also useful to estimate the average deviation of the delay, vi :
The estimates di and vi are calculated for every received packet, although they are only used at the beginning of a talk spurt.
For first packet in talk spurt, playout time is:
where K is a positive constant.
Remaining packets in talkspurt are played out periodically

## Slide 39: Adaptive Playout, III
Q: How does receiver determine whether packet is first in a talkspurt?
If no loss, receiver looks at successive timestamps.
  difference of successive stamps > 20 msec -->talk spurt begins.
With loss possible, receiver must look at both time stamps and sequence numbers.
  difference of successive stamps > 20 msec and sequence numbers without gaps --> talk spurt begins.

## Slide 40: Recovery from packet loss (1)
forward error correction (FEC): simple scheme
for every group of n chunks create a redundant chunk by exclusive OR-ing the n original chunks
send out n+1 chunks, increasing the bandwidth by factor 1/n.
can reconstruct the original n chunks if there is at most one lost chunk from the n+1 chunks
Playout delay needs to be fixed to the time to receive all n+1 packets
Tradeoff:
  increase n, less bandwidth waste
  increase n, longer playout delay
  increase n, higher probability that 2 or more chunks will be lost

## Slide 41: Recovery from packet loss (2)
2nd FEC scheme
“piggyback lower quality stream”
send lower resolution audio stream as the redundant information
for example, nominal stream PCM at 64 kbps and redundant stream GSM at 13 kbps.
Whenever there is non-consecutive loss, the receiver can conceal the loss.
Can also append (n-1)st and (n-2)nd low-bit rate chunk

## Slide 42: Recovery from packet loss (3)
Interleaving
chunks are broken up into smaller units
for example, 4 5 msec units per chunk
Packet contains small units from different chunks
if packet is lost, still have most of every chunk
has no redundancy overhead
but adds to playout delay

## Slide 43: Summary: Internet Multimedia: bag of tricks
use UDP to avoid TCP congestion control (delays) for time-sensitive traffic
client-side adaptive playout delay: to compensate for delay
server side matches stream bandwidth to available client-to-server path bandwidth
  chose among pre-encoded stream rates
  dynamic server encoding rate
error recovery (on top of UDP)
  FEC, interleaving
  retransmissions, time permitting
  conceal errors: repeat nearby data

## Slide 44: Chapter 7 outline
7.1 Multimedia Networking Applications
7.2 Streaming stored audio and video
7.3 Real-time Multimedia: Internet Phone study
7.4 Protocols for Real-Time Interactive Applications
  RTP,RTCP,SIP
7.5 Distributing Multimedia: content distribution networks
7.6 Beyond Best Effort
7.7 Scheduling and Policing Mechanisms
7.8 Integrated Services and Differentiated Services
7.9 RSVP

## Slide 45: Real-Time Protocol (RTP)
RTP specifies a packet structure for packets carrying audio and video data
RFC 1889.
RTP packet provides
  payload type identification
  packet sequence numbering
  timestamping
RTP runs in the end systems.
RTP packets are encapsulated in UDP segments
Interoperability: If two Internet phone applications run RTP, then they may be able to work together

## Slide 46: RTP runs on top of UDP
RTP libraries provide a transport-layer interface
that extend UDP:
  port numbers, IP addresses
  payload type identification
  packet sequence numbering
  time-stamping

## Slide 47: RTP Example
Consider sending 64 kbps PCM-encoded voice over RTP.
Application collects the encoded data in chunks, e.g., every 20 msec = 160 bytes in a chunk.
The audio chunk along with the RTP header form the RTP packet, which is encapsulated into a UDP segment.
RTP header indicates type of audio encoding in each packet
  sender can change encoding during a conference.
RTP header also contains sequence numbers and timestamps.

## Slide 48: RTP and QoS
RTP does not provide any mechanism to ensure timely delivery of data or provide other quality of service guarantees.
RTP encapsulation is only seen at the end systems: it is not seen by intermediate routers.
  Routers providing best-effort service do not make any special effort to ensure that RTP packets arrive at the destination in a timely matter.

## Slide 49: RTP Header
Payload Type (7 bits): Indicates type of encoding currently being used. If sender changes encoding in middle of conference, sender
informs the receiver through this payload type field.
  Payload type 0: PCM mu-law, 64 kbps
  Payload type 3, GSM, 13 kbps
  Payload type 7, LPC, 2.4 kbps
  Payload type 26, Motion JPEG
  Payload type 31. H.261
  Payload type 33, MPEG2 video
Sequence Number (16 bits): Increments by one for each RTP packet
sent, and may be used to detect packet loss and to restore packet
sequence.

## Slide 50: RTP Header (2)
Timestamp field (32 bytes long). Reflects the sampling instant of the first byte in the RTP data packet.
  For audio, timestamp clock typically increments by one for each sampling period (for example, each 125 usecs for a 8 KHz sampling clock)
  if application generates chunks of 160 encoded samples, then timestamp increases by 160 for each RTP packet when source is active. Timestamp clock continues to increase at constant rate when source is inactive.
SSRC field (32 bits long). Identifies the source of the RTP stream. Each stream in a RTP session should have a distinct SSRC.

## Slide 51: RTSP/RTP Programming Assignment
Build a server that encapsulates stored video frames into RTP packets
  grab video frame, add RTP headers, create UDP segments, send segments to UDP socket
  include seq numbers and time stamps
  client RTP provided for you
Also write the client side of RTSP
  issue play and pause commands
  server RTSP provided for you

## Slide 52: Real-Time Control Protocol (RTCP)
Works in conjunction with RTP.
Each participant in RTP session periodically transmits RTCP control packets to all other participants.
Each RTCP packet contains sender and/or receiver reports
  report statistics useful to application
Statistics include number of packets sent, number of packets lost, interarrival jitter, etc.
Feedback can be used to control performance
  Sender may modify its transmissions based on feedback

## Slide 53: RTCP - Continued
- For an RTP session there is typically a single multicast address; all RTP and RTCP packets belonging to the session use the multicast address.
- RTP and RTCP packets are distinguished from each other through the use of
distinct port numbers.
- To limit traffic, each participant reduces his RTCP traffic as the number of conference participants increases.

## Slide 54: RTCP Packets
Receiver report packets:
fraction of packets lost, last sequence number, average interarrival jitter.
Sender report packets:
SSRC of the RTP stream, the current time, the number of packets sent, and the number of bytes sent.
Source description packets:
e-mail address of sender, sender's name, SSRC of associated RTP stream.
Provide mapping between the SSRC and the user/host name.

## Slide 55: Synchronization of Streams
RTCP can synchronize different media streams within a RTP session.
Consider videoconferencing app for which each sender generates one RTP stream for video and one for audio.
Timestamps in RTP packets tied to the video and audio sampling clocks
  not tied to the wall-clock time
Each RTCP sender-report packet contains (for the most recently generated packet in the associated RTP stream):
  timestamp of the RTP packet
  wall-clock time for when packet was created.
Receivers can use this association to synchronize the playout of audio and video.

## Slide 56: RTCP Bandwidth Scaling
RTCP attempts to limit its traffic to 5% of the session bandwidth.
Example
Suppose one sender, sending video at a rate of 2 Mbps. Then RTCP attempts to limit its traffic to 100 Kbps.
RTCP gives 75% of this rate to the receivers; remaining 25% to the sender
The 75 kbps is equally shared among receivers:
  With R receivers, each receiver gets to send RTCP traffic at 75/R kbps.
Sender gets to send RTCP traffic at 25 kbps.
Participant determines RTCP packet transmission period by calculating avg RTCP packet size (across the entire session) and dividing by allocated rate.

## Slide 57: SIP
Session Initiation Protocol
Comes from IETF
SIP long-term vision
All telephone calls and video conference calls take place over the Internet
People are identified by names or e-mail addresses, rather than by phone numbers.
You can reach the callee, no matter where the callee roams, no matter what IP device the callee is currently using.

## Slide 58: SIP Services
Setting up a call
  Provides mechanisms for caller to let callee know she wants to establish a call
  Provides mechanisms so that caller and callee can agree on media type and encoding.
  Provides mechanisms to end call.
Determine current IP address of callee.
  Maps mnemonic identifier to current IP address
Call management
  Add new media streams during call
  Change encoding during call
  Invite others
  Transfer and hold calls

## Slide 59: Setting up a call to a known IP address
Alice’s SIP invite message indicates her port number & IP address. Indicates encoding that Alice prefers to receive (PCM ulaw)
Bob’s 200 OK message indicates his port number, IP address & preferred encoding (GSM)
SIP messages can be sent over TCP or UDP; here sent over RTP/UDP.
Default SIP port number is 5060.

## Slide 60: Setting up a call (more)
Codec negotiation:
  Suppose Bob doesn’t have PCM ulaw encoder.
  Bob will instead reply with 606 Not Acceptable Reply and list encoders he can use.
  Alice can then send a new INVITE message, advertising an appropriate encoder.
Rejecting the call
  Bob can reject with replies “busy,” “gone,” “payment required,” “forbidden”.
Media can be sent over RTP or some other protocol.

## Slide 61: Example of SIP message
INVITE sip:bob@domain.com SIP/2.0
Via: SIP/2.0/UDP 167.180.112.24
From: sip:alice@hereway.com
To: sip:bob@domain.com
Call-ID: a2e3a@pigeon.hereway.com
Content-Type: application/sdp
Content-Length: 885
c=IN IP4 167.180.112.24
m=audio 38060 RTP/AVP 0
Notes:
HTTP message syntax
sdp = session description protocol
Call-ID is unique for every call.
Here we don’t know
Bob’s IP address.
Intermediate SIP servers will be necessary.
Alice sends and receives SIP messages using the SIP default port number 506.
Alice specifies in Via: header that SIP client sends and receives SIP messages over UDP

## Slide 62: Name translation and user locataion
Caller wants to call callee, but only has callee’s name or e-mail address.
Need to get IP address of callee’s current host:
  user moves around
  DHCP protocol
  user has different IP devices (PC, PDA, car device)
Result can be based on:
  time of day (work, home)
  caller (don’t want boss to call you at home)
  status of callee (calls sent to voicemail when callee is already talking to someone)
Service provided by SIP servers:
SIP registrar server
SIP proxy server

## Slide 63: SIP Registrar
REGISTER sip:domain.com SIP/2.0
Via: SIP/2.0/UDP 193.64.210.89
From: sip:bob@domain.com
To: sip:bob@domain.com
Expires: 3600
When Bob starts SIP client, client sends SIP REGISTER message to Bob’s registrar server
(similar function needed by Instant Messaging)
Register Message:

## Slide 64: SIP Proxy
Alice sends invite message to her proxy server
  contains address sip:bob@domain.com
Proxy responsible for routing SIP messages to callee
  possibly through multiple proxies.
Callee sends response back through the same set of proxies.
Proxy returns SIP response message to Alice
  contains Bob’s IP address
Note: proxy is analogous to local DNS server

## Slide 65: Example
Caller jim@umass.edu with places a
call to keith@upenn.edu
(1) Jim sends INVITE message to umass SIP proxy. (2) Proxy forwards request to upenn registrar server. (3) upenn server returns redirect response, indicating that it should try keith@eurecom.fr
(4) umass proxy sends INVITE to eurecom registrar. (5) eurecom registrar forwards INVITE to 197.87.54.21, which is running keith’s SIP client. (6-8) SIP response sent back (9) media sent directly
between clients.
Note: also a SIP ack message, which is not shown.

## Slide 66: Comparison with H.323
H.323 is another signaling protocol for real-time, interactive
H.323 is a complete, vertically integrated suite of protocols for multimedia conferencing: signaling, registration, admission control, transport and codecs.
SIP is a single component. Works with RTP, but does not mandate it. Can be combined with other protocols and services.
H.323 comes from the ITU (telephony).
SIP comes from IETF: Borrows much of its concepts from HTTP. SIP has a Web flavor, whereas H.323 has a telephony flavor.
SIP uses the KISS principle: Keep it simple stupid.

## Slide 67: Chapter 7 outline
7.1 Multimedia Networking Applications
7.2 Streaming stored audio and video
7.3 Real-time Multimedia: Internet Phone study
7.4 Protocols for Real-Time Interactive Applications
  RTP,RTCP,SIP
7.5 Distributing Multimedia: content distribution networks
7.6 Beyond Best Effort
7.7 Scheduling and Policing Mechanisms
7.8 Integrated Services and Differentiated Services
7.9 RSVP

## Slide 68: Content distribution networks (CDNs)
Content replication
Challenging to stream large files (e.g., video) from single origin server in real time
Solution: replicate content at hundreds of servers throughout Internet
  content downloaded to CDN servers ahead of time
  placing content “close” to user avoids impairments (loss, delay) of sending content over long paths
  CDN server typically in edge/access network
origin server
in North America
CDN distribution node
CDN server
in S. America
CDN server
in Europe
CDN server
in Asia

## Slide 69: Content distribution networks (CDNs)
Content replication
CDN (e.g., Akamai) customer is the content provider (e.g., CNN)
CDN replicates customers’ content in CDN servers. When provider updates content, CDN updates servers
origin server
in North America
CDN distribution node
CDN server
in S. America
CDN server
in Europe
CDN server
in Asia

## Slide 70: CDN example
origin server (www.foo.com)
distributes HTML
replaces:
http://www.foo.com/sports.ruth.gif
with http://www.cdn.com/www.foo.com/sports/ruth.gif
HTTP request for
www.foo.com/sports/sports.html
DNS query for www.cdn.com
HTTP request for
www.cdn.com/www.foo.com/sports/ruth.gif
1
2
3
Origin server
CDNs authoritative
DNS server
Nearby
CDN server
CDN company (cdn.com)
distributes gif files
uses its authoritative DNS server to route redirect requests

## Slide 71: More about CDNs
routing requests
CDN creates a “map”, indicating distances from leaf ISPs and CDN nodes
when query arrives at authoritative DNS server:
  server determines ISP from which query originates
  uses “map” to determine best CDN server
CDN nodes create application-layer overlay network

## Slide 72: Chapter 7 outline
7.1 Multimedia Networking Applications
7.2 Streaming stored audio and video
7.3 Real-time Multimedia: Internet Phone study
7.4 Protocols for Real-Time Interactive Applications
  RTP,RTCP,SIP
7.5 Distributing Multimedia: content distribution networks
7.6 Beyond Best Effort
7.7 Scheduling and Policing Mechanisms
7.8 Integrated Services and Differentiated Services
7.9 RSVP

## Slide 73: Improving QOS in IP Networks
Thus far: “making the best of best effort”
Future: next generation Internet with QoS guarantees
  RSVP: signaling for resource reservations
  Differentiated Services: differential guarantees
  Integrated Services: firm guarantees
simple model for sharing and congestion studies:

## Slide 74: Principles for QOS Guarantees
Example: 1MbpsI P phone, FTP share 1.5 Mbps link.
  bursts of FTP can congest router, cause audio loss
  want to give priority to audio over FTP
packet marking needed for router to distinguish between different classes; and new router policy to treat packets accordingly
Principle 1

## Slide 75: Principles for QOS Guarantees (more)
what if applications misbehave (audio sends higher than declared rate)
  policing: force source adherence to bandwidth allocations
marking and policing at network edge:
  similar to ATM UNI (User Network Interface)
provide protection (isolation) for one class from others
Principle 2

## Slide 76: Principles for QOS Guarantees (more)
Allocating fixed (non-sharable) bandwidth to flow: inefficient use of bandwidth if flows doesn’t use its allocation
While providing isolation, it is desirable to use
resources as efficiently as possible
Principle 3

## Slide 77: Principles for QOS Guarantees (more)
Basic fact of life: can not support traffic demands beyond link capacity
Call Admission: flow declares its needs, network may
block call (e.g., busy signal) if it cannot meet needs
Principle 4

## Slide 78: Summary of QoS Principles
Let’s next look at mechanisms for achieving this ….

## Slide 79: Chapter 7 outline
7.1 Multimedia Networking Applications
7.2 Streaming stored audio and video
7.3 Real-time Multimedia: Internet Phone study
7.4 Protocols for Real-Time Interactive Applications
  RTP,RTCP,SIP
7.5 Distributing Multimedia: content distribution networks
7.6 Beyond Best Effort
7.7 Scheduling and Policing Mechanisms
7.8 Integrated Services and Differentiated Services
7.9 RSVP

## Slide 80: Scheduling And Policing Mechanisms
scheduling: choose next packet to send on link
FIFO (first in first out) scheduling: send in order of arrival to queue
  real-world example?
  discard policy: if packet arrives to full queue: who to discard?
    Tail drop: drop arriving packet
    priority: drop/remove on priority basis
    random: drop/remove randomly

## Slide 81: Scheduling Policies: more
Priority scheduling: transmit highest priority queued packet
multiple classes, with different priorities
  class may depend on marking or other header info, e.g. IP source/dest, port numbers, etc..
  Real world example?

## Slide 82: Scheduling Policies: still more
round robin scheduling:
multiple classes
cyclically scan class queues, serving one from each class (if available)
real world example?

## Slide 83: Scheduling Policies: still more
Weighted Fair Queuing:
generalized Round Robin
each class gets weighted amount of service in each cycle
real-world example?

## Slide 84: Policing Mechanisms
Goal: limit traffic to not exceed declared parameters
Three common-used criteria:
(Long term) Average Rate: how many pkts can be sent per unit time (in the long run)
  crucial question: what is the interval length: 100 packets per sec or 6000 packets per min have same average!
Peak Rate: e.g., 6000 pkts per min. (ppm) avg.; 1500 ppm peak rate
(Max.) Burst Size: max. number of pkts sent consecutively (with no intervening idle)

## Slide 85: Policing Mechanisms
Token Bucket: limit input to specified Burst Size and Average Rate.
bucket can hold b tokens
tokens generated at rate r token/sec unless bucket full
over interval of length t: number of packets admitted less than or equal to (r t + b).

## Slide 86: Policing Mechanisms (more)
token bucket, WFQ combine to provide guaranteed upper bound on delay, i.e., QoS guarantee!
WFQ
token rate, r
bucket size, b
per-flow
rate, R
D = b/R
max
arriving
traffic

## Slide 87: Chapter 7 outline
7.1 Multimedia Networking Applications
7.2 Streaming stored audio and video
7.3 Real-time Multimedia: Internet Phone study
7.4 Protocols for Real-Time Interactive Applications
  RTP,RTCP,SIP
7.5 Distributing Multimedia: content distribution networks
7.6 Beyond Best Effort
7.7 Scheduling and Policing Mechanisms
7.8 Integrated Services and Differentiated Services
7.9 RSVP

## Slide 88: IETF Integrated Services
architecture for providing QOS guarantees in IP networks for individual application sessions
resource reservation: routers maintain state info (a la VC) of allocated resources, QoS req’s
admit/deny new call setup requests:
Question: can newly arriving flow be admitted
with performance guarantees while not violated
QoS guarantees made to already admitted flows?

## Slide 89: Intserv: QoS guarantee scenario
Resource reservation
  call setup, signaling (RSVP)
  traffic, QoS declaration
  per-element admission control
  QoS-sensitive scheduling (e.g., WFQ)
request/
reply

## Slide 90: Call Admission
Arriving session must :
declare its QOS requirement
  R-spec: defines the QOS being requested
characterize traffic it will send into network
  T-spec: defines traffic characteristics
signaling protocol: needed to carry R-spec and T-spec to routers (where reservation is required)
  RSVP

## Slide 91: Intserv QoS: Service models [rfc2211, rfc 2212]
Guaranteed service:
worst case traffic arrival: leaky-bucket-policed source
simple (mathematically provable) bound on delay [Parekh 1992, Cruz 1988]
Controlled load service:
"a quality of service closely approximating the QoS that same flow would receive from an unloaded network element."
WFQ
token rate, r
bucket size, b
per-flow
rate, R
D = b/R
max
arriving
traffic

## Slide 92: IETF Differentiated Services
Concerns with Intserv:
Scalability: signaling, maintaining per-flow router state difficult with large number of flows
Flexible Service Models: Intserv has only two classes. Also want “qualitative” service classes
  “behaves like a wire”
  relative service distinction: Platinum, Gold, Silver
Diffserv approach:
simple functions in network core, relatively complex functions at edge routers (or hosts)
Do’t define define service classes, provide functional components to build service classes

## Slide 93: Diffserv Architecture
Edge router:
per-flow traffic management
marks packets as in-profile and out-profile
Core router:
per class traffic management
buffering and scheduling based on marking at edge
preference given to in-profile packets
Assured Forwarding
scheduling
.
.
.
r
b
marking

## Slide 94
Edge-router Packet Marking
class-based marking: packets of different classes marked differently
intra-class marking: conforming portion of flow marked differently than non-conforming one
profile: pre-negotiated rate A, bucket size B
packet marking at edge based on per-flow profile
Possible usage of marking:
User packets
Rate A
B

## Slide 95: Classification and Conditioning
Packet is marked in the Type of Service (TOS) in IPv4, and Traffic Class in IPv6
6 bits used for Differentiated Service Code Point (DSCP) and determine PHB that the packet will receive
2 bits are currently unused

## Slide 96: Classification and Conditioning
may be desirable to limit traffic injection rate of some class:
user declares traffic profile (e.g., rate, burst size)
traffic metered, shaped if non-conforming

## Slide 97: Forwarding (PHB)
PHB result in a different observable (measurable) forwarding performance behavior
PHB does not specify what mechanisms to use to ensure required PHB performance behavior
Examples:
  Class A gets x% of outgoing link bandwidth over time intervals of a specified length
  Class A packets leave first before packets from class B

## Slide 98: Forwarding (PHB)
PHBs being developed:
Expedited Forwarding: pkt departure rate of a class equals or exceeds specified rate
  logical link with a minimum guaranteed rate
Assured Forwarding: 4 classes of traffic
  each guaranteed minimum amount of bandwidth
  each with three drop preference partitions

## Slide 99: Chapter 7 outline
7.1 Multimedia Networking Applications
7.2 Streaming stored audio and video
7.3 Real-time Multimedia: Internet Phone study
7.4 Protocols for Real-Time Interactive Applications
  RTP,RTCP,SIP
7.5 Distributing Multimedia: content distribution networks
7.6 Beyond Best Effort
7.7 Scheduling and Policing Mechanisms
7.8 Integrated Services and Differentiated Services
7.9 RSVP

## Slide 100: Signaling in the Internet
connectionless (stateless) forwarding by IP routers
best effort service
no network signaling protocols
in initial IP design
+
=
New requirement: reserve resources along end-to-end path (end system, routers) for QoS for multimedia applications
RSVP: Resource Reservation Protocol [RFC 2205]
  “ … allow users to communicate requirements to network in robust and efficient way.” i.e., signaling !
earlier Internet Signaling protocol: ST-II [RFC 1819]

## Slide 101: RSVP Design Goals
accommodate heterogeneous receivers (different bandwidth along paths)
accommodate different applications with different resource requirements
make multicast a first class service, with adaptation to multicast group membership
leverage existing multicast/unicast routing, with adaptation to changes in underlying unicast, multicast routes
control protocol overhead to grow (at worst) linear in # receivers
modular design for heterogeneous underlying technologies

## Slide 102: RSVP: does not…
specify how resources are to be reserved
  rather: a mechanism for communicating needs
determine routes packets will take
  that’s the job of routing protocols
  signaling decoupled from routing
interact with forwarding of packets
  separation of control (signaling) and data (forwarding) planes

## Slide 103: RSVP: overview of operation
senders, receiver join a multicast group
  done outside of RSVP
  senders need not join group
sender-to-network signaling
  path message: make sender presence known to routers
  path teardown: delete sender’s path state from routers
receiver-to-network signaling
  reservation message: reserve resources from sender(s) to receiver
  reservation teardown: remove receiver reservations
network-to-end-system signaling
  path error
  reservation error

## Slide 104: Path msgs: RSVP sender-to-network signaling
path message contents:
  address: unicast destination, or multicast group
  flowspec: bandwidth requirements spec.
  filter flag: if yes, record identities of upstream senders (to allow packets filtering by source)
  previous hop: upstream router/host ID
  refresh time: time until this info times out
path message: communicates sender info, and reverse-path-to-sender routing info
  later upstream forwarding of receiver reservations

## Slide 105: RSVP: simple audio conference
H1, H2, H3, H4, H5 both senders and receivers
multicast group m1
no filtering: packets from any sender forwarded
audio rate: b
only one multicast routing tree possible
H2
H5
H3
H4
H1
R1
R2
R3

## Slide 106: RSVP: building up path state
in
out
in
out
in
out
H1, …, H5 all send path messages on m1:
(address=m1, Tspec=b, filter-spec=no-filter,refresh=100)
Suppose H1 sends first path message
H2
H5
H3
H4
H1
R1
R2
R3
L1
L2
L3
L4
L5
L6
L7
L5
L7
L6
L1
L2
L6
L3
L7
L4
m1:
m1:
m1:

## Slide 107: RSVP: building up path state
in
out
in
out
in
out
next, H5 sends path message, creating more state in routers
H2
H5
H3
H4
H1
R1
R2
R3
L1
L2
L3
L4
L5
L6
L7
L5
L7
L6
L1
L2
L6
L3
L7
L4
L5
L6
L1
L6
m1:
m1:
m1:

## Slide 108: RSVP: building up path state
in
out
in
out
in
out
H2, H3, H5 send path msgs, completing path state tables
H2
H5
H3
H4
H1
R1
R2
R3
L1
L2
L3
L4
L5
L6
L7
L5
L7
L6
L1
L2
L6
L3
L7
L4
L5
L6
L1
L6
L7
L4
L3
L7
L2
m1:
m1:
m1:

## Slide 109: reservation msgs: receiver-to-network signaling
reservation message contents:
  desired bandwidth:
  filter type:
    no filter: any packets address to multicast group can use reservation
    fixed filter: only packets from specific set of senders can use reservation
    dynamic filter: senders who’s p[ackets can be forwarded across link will change (by receiver choce) over time.
  filter spec
reservations flow upstream from receiver-to-senders, reserving resources, creating additional, receiver-related state at routers

## Slide 110: RSVP: receiver reservation example 1
H1 wants to receive audio from all other senders
H1 reservation msg flows uptree to sources
H1 only reserves enough bandwidth for 1 audio stream
reservation is of type “no filter” – any sender can use reserved bandwidth
H2
H5
H3
H4
H1
R1
R2
R3
L1
L2
L3
L4
L5
L6
L7

## Slide 111: RSVP: receiver reservation example 1
in
out
H1 reservation msgs flows uptree to sources
routers, hosts reserve bandwidth b needed on downstream links towards H1
H2
H5
H3
H4
H1
R1
R2
R3
L1
L2
L3
L4
L5
L6
L7
L1
L2
L6
L6
L1
(b)
in
out
L5
L6
L7
L7
L5
(b)
L6
in
out
L3
L4
L7
L7
L3
(b)
L4
L2
b
b
b
b
b
b
b
m1:
m1:
m1:

## Slide 112: RSVP: receiver reservation example 1 (more)
in
out
next, H2 makes no-filter reservation for bandwidth b
H2 forwards to R1, R1 forwards to H1 and R2 (?)
R2 takes no action, since b already reserved on L6
H2
H5
H3
H4
H1
R1
R2
R3
L1
L2
L3
L4
L5
L6
L7
L1
L2
L6
L6
L1
(b)
in
out
L5
L6
L7
L7
L5
(b)
L6
in
out
L3
L4
L7
L7
L3
(b)
L4
L2
b
b
b
b
b
b
b
b
b
(b)
m1:
m1:
m1:

## Slide 113: RSVP: receiver reservation: issues
in
out
What if multiple senders (e.g., H3, H4, H5) over link (e.g., L6)?
arbitrary interleaving of packets
L6 flow policed by leaky bucket: if H3+H4+H5 sending rate exceeds b, packet loss will occur
H2
H5
H3
H4
H1
R1
R2
R3
L1
L2
L3
L4
L5
L6
L7
L1
L2
L6
L6
L1
(b)
in
out
L5
L6
L7
L7
L5
(b)
L6
in
out
L3
L4
L7
L7
L3
(b)
L4
L2
b
b
b
b
b
b
b
b
b
(b)
m1:
m1:
m1:

## Slide 114: RSVP: example 2
H1, H4 are only senders
  send path messages as before, indicating filtered reservation
  Routers store upstream senders for each upstream link
H2 will want to receive from H4 (only)
H2
H3
H4
H1
R1
R2
R3
L1
L2
L3
L4
L6
L7
H2
H3
L2
L3

## Slide 115: RSVP: example 2
H1, H4 are only senders
  send path messages as before, indicating filtered reservation
H2
H3
H4
H1
R1
R3
L1
L2
L3
L4
L6
L7
H2
H3
L2
L3
L2(H1-via-H1 ; H4-via-R2 )
L6(H1-via-H1 )
L1(H4-via-R2 )
in
out
L6(H4-via-R3 )
L7(H1-via-R1 )
in
out
L1, L6
L6, L7
L3(H4-via-H4 ; H1-via-R3 )
L4(H1-via-R2 )
L7(H4-via-H4 )
in
out
L4, L7
R2

## Slide 116: RSVP: example 2
receiver H2 sends reservation message for source H4 at bandwidth b
  propagated upstream towards H4, reserving b
H2
H3
H4
H1
R1
R3
L1
L2
L3
L4
L6
L7
H2
H3
L2
L3
L2(H1-via-H1 ;H4-via-R2 )
L6(H1-via-H1 )
L1(H4-via-R2 )
in
out
L6(H4-via-R3 )
L7(H1-via-R1 )
in
out
L1, L6
L6, L7
L3(H4-via-H4 ; H1-via-R2 )
L4(H1-via-62 )
L7(H4-via-H4 )
in
out
L4, L7
R2
(b)
(b)
(b)
L1
b
b
b
b

## Slide 117: RSVP: soft-state
senders periodically resend path msgs to refresh (maintain) state
receivers periodically resend resv msgs to refresh (maintain) state
path and resv msgs have TTL field, specifying refresh interval
H2
H3
H4
H1
R1
R3
L1
L2
L3
L4
L6
L7
H2
H3
L2
L3
L2(H1-via-H1 ;H4-via-R2 )
L6(H1-via-H1 )
L1(H4-via-R2 )
in
out
L6(H4-via-R3 )
L7(H1-via-R1 )
in
out
L1, L6
L6, L7
L3(H4-via-H4 ; H1-via-R3 )
L4(H1-via-62 )
L7(H4-via-H4 )
in
out
L4, L7
R2
(b)
(b)
(b)
L1
b
b
b
b

## Slide 118: RSVP: soft-state
suppose H4 (sender) leaves without performing teardown
H2
H3
H4
H1
R1
R3
L1
L2
L3
L4
L6
L7
H2
H3
L2
L3
L2(H1-via-H1 ;H4-via-R2 )
L6(H1-via-H1 )
L1(H4-via-R2 )
in
out
L6(H4-via-R3 )
L7(H1-via-R1 )
in
out
L1, L6
L6, L7
L3(H4-via-H4 ; H1-via-R3 )
L4(H1-via-62 )
L7(H4-via-H4 )
in
out
L4, L7
R2
(b)
(b)
(b)
L1
b
b
b
b
eventually state in routers will timeout and disappear!
gone
fishing!

## Slide 119: The many uses of reservation/path refresh
recover from an earlier lost refresh message
  expected time until refresh received must be longer than timeout interval! (short timer interval desired)
Handle receiver/sender that goes away without teardown
  Sender/receiver state will timeout and disappear
Reservation refreshes will cause new reservations to be made to a receiver from a sender who has joined since receivers last reservation refresh
  E.g., in previous example, H1 is only receiver, H3 only sender. Path/reservation messages complete, data flows
  H4 joins as sender, nothing happens until H3 refreshes reservation, causing R3 to forward reservation to H4, which allocates bandwidth

## Slide 120: RSVP: reflections
multicast as a “first class” service
receiver-oriented reservations
use of soft-state

## Slide 121: Multimedia Networking: Summary
multimedia applications and requirements
making the best of today’s best effort service
scheduling and policing mechanisms
next generation Internet: Intserv, RSVP, Diffserv